My customer has a cracked 2-inch LB Conduit Body. Do you have any suggestions or a repair kit for this problem?

The LB needs to be replaced. If it is just a cover, a standard LB can be purchased and the cover removed from it. If it is, the body that is cracked than the whole LB body should be replaced which means that it has to be cut from the conduit system after the conductors have been pulled. Since the conduit is solvent cemented into the LB some raceway may need to be replaced too.

Is it possible to get replacement covers for box E989RRX?

I'm sorry, but we only sell the nonmetallic molded junction box as a complete unit: box, lid, gasket, and screws.

We will specify an end bell for schedule 80, 4" electrical conduit.  What is your product number?  Is this a long end bell, other characteristics?

A standard PVC end bell for 4" Schedule 80 would be part number E997N. We no longer offer a 4" long end bell since this bell end handled the majority of applications.